## Slide 1: YCAT – Yaesu Computer Assisted Transceiver
Yaesu HF Radio CAT control demo
Steve Ollmann – KC5NK

## Slide 2: Why YCAT?
Started as a way of learning my FT-891 with limited menus
Control and Monitor radio over enhanced USB serial interface
Used to control most common features of the radio
Provide User defined functionality
Access to all meters at once
Program VFO memories
Simple logbook, exports ADIF format (Even POTA)
User selectable mapping views (requires vendor Keys for most maps)

## Slide 3: YCAT - Origins
Bought FT-891 at beginning of Covid for “keeping in touch” with the world
Noticed it had serial interface (CAT) which is what I do along with GPS
Dabbled turning rig on and off, then added more features to learn about the FT-891.
Eventually, it started taking form as a Rig Control application
Started adding new radios (FT-991a, FT-dx10, FT-710, FT-dx3000, etc.)
Reluctantly added a QSO logger and added POTA features for drag-n-drop into POTA.app
Mapping allows me to find my own grid square without GPS and find bearing to DX stations if I needed to point a beam towards them.

## Slide 4: What is YCAT?
Rig Control
Customizable buttons
All Meters display (relocatable)
RIG / GPS / SDR and WSJT-x interfaces
GPS computes 6-digit grid and PC time
SDR interface works with RSP-dx, etc.
VFO Memory read/write and file read/save
HamDB and QRZ call sign lookup
Voice Memory record/verify/send
CW control, memory record/send
Microphone equalizer settings
Logger (regular / POTA)
POTA spot viewing (filtering)
Mapping with helpful features
Spectrum Scope management for supported rigs
Windows 32-bit application

## Slide 5: YCAT – Main Operating Screen

## Slide 6: YCAT – Operation Info (Default tab)
My Information
  Enter station call sign
  Rig field should auto configure after radio starts communicating
  Antenna field is optional
  My Grid: this field will auto populate with a GPS dongle. Manually enter if no GPS configured.
POTA
  Check if activating POTA, enter park number and park name
WSJT-x Search
  Check “Enable Search” for audible beep for decoding “Search Term”

## Slide 7: YCAT – Serial Comms
Yaesu CAT Serial
  Use Enhanced port
EXT CAT (WSJT-X)
  Requires virtual serial cable
  In this case (COM70 / COM71)
SDR CAT – emulates Kenwood TS480
  Requires virtual serial cable
  2-way communication with SDR Play / SDR Uno
GPS Serial
  Sync PC Time with GPS Time (requires YCAT to run as Admin)
  Shows current Latitude / Longitude and 6-digit Grid Square
WSJT-X UDP
  Allows receiving WSJT-X log information for YCAT logger
  Must match IP and Port number.
  Supports Multi-Cast

## Slide 8: YCAT – Main Screen
Many indicators are also controls
  Power – turns radio ON/OFF
  TNR EN – turns tuner ON/OFF
  TUNE – initiates a tune cycle
  TX ON – “keys” and “unkeys” transmitter
RF Pwr (watts) – TX power setting
Time settings
  LCL – shows local time from PC
  UTC – shows UTC time from PC
  GPS – shows GPS time (UTC)
    Requires optional GPS receiver

## Slide 9: YCAT – Main Screen
VFO A Frequency
  Memory Tag – user defined
  Mem Channel indicator
VFO B Frequency
VFO Controls
  Auto Down – hold to decrease VFO A
  Auto Up – hold to increase VFO A
  LOCK – Locks the VFO
  Step Down – press to decrement VFO
  Step Up – press to increment VFO
  FINE (FAST) – controls VFO steps
  SPLIT – turns VFO A/B split mode on/off
S-meter – shows radio S readings (with peak indicator)

## Slide 10: YCAT – Main Screen Modes (Legacy)
Mode select
  SSB
  CW
  RTTY
  DATA
  AM
  AM Narrow
  FM
  FM Narrow
  C4FM (FT-991 only)

## Slide 11: YCAT – Mode Selection (new)
Click mode section under VFO-A to bring up menu
Select Mode and menu closes automatically
Similar to FT-710 screen operation
  Works the same for all rigs

## Slide 12: YCAT - User Defined Buttons (CAT COMMANDS)
Five ( 5 ) buttons are available for the user to add their own features.
Choose whether buttons are visible, what text to display, and the underlying CAT commands
CAT Commands can be concatenated
Reference the Yaesu CAT Manual for your rig.
Configure in PRESETS tab

## Slide 13: YCAT – Voice Memory
Buttons have customizable text
Configured in Voice Mem tab
Defaults to SEND
Can Record, Verify, and Send when pressed (Voice Mem Tab)

## Slide 14: YCAT – Band Selection
Simple Band Up and Band Down buttons
Select Band button allows choosing the band to go to:
Menu stays up until you choose band or cancel

## Slide 15: YCAT – Main : Grid Square
When GPS is connected it automatically computes a 6-digit grid square
Auto populates Operation Info – Grid Square field
Syncs radio clock automatically
Syncs PC clock (YCAT must be run as Admin for write to system clock permission)

## Slide 16: YCAT – Radio Control Tab
Organized Audio to RF from left to right
VFO / Memory operation on the furthest right-hand side

## Slide 17: YCAT – Presets Tab
TOT – TX Timeout Timer
User Controls
Display Settings
Tuner Settings
Visual Theme
Mapping API Key storage.

## Slide 18: YCAT – Meters Tab
Display all meters at once
Voltage is real-time, all others are active during transmission.

## Slide 19: YCAT – Memory Tab
Programming for VFO Memory with “TAGS”
Read/Write with your Rig
Read/Write with a file

## Slide 20: YCAT – Voice Memory Tab
Allows user to create voice memory, customize buttons and control record, verify and send behavior for the five ( 5 ) voice memories in the Yaesu radio.

## Slide 21: YCAT – CW Settings Tab
Used for configure Yaesu radio CW Memory parameters
Customize CW memory slots, adjust MON level, Keyer Pitch and Keyer Speed.

## Slide 22: YCAT – Mic Settings Tab
Set Mic Equalizer settings for PRC disabled / PRC enabled modes
Set Transmit bandwidth settings for SSB, AM, and Data

## Slide 23: YCAT – POTA Spots Tab
Requires internet connection
Press “Show POTA Spots” button
POTA spots spreadsheet pops up
Filter by Mode is most helpful
Scroll or select a row tunes VFO
  Auto populates in Log Book tab

## Slide 24: YCAT – Logging from POTA Spots
Clicking on a row in POTA Spots grid will auto populate Log Book

## Slide 25: YCAT – POTA Logbook Setup
Manually enter your park information in POTA section of OPERATION INFO tab

## Slide 26: YCAT - POTA Logbook Setup, continued
Switch to Log Book tab
Call sign lookup choices are: None, HamDB, and QRZ
Notice addition of visual cues for park information
Enter call sign, if Call Lookup is enabled, a popup will show DX call information

## Slide 27: YCAT – POTA Logging w/callsign lookup

## Slide 28: YCAT – POTA Logging

## Slide 29: YCAT – Contact Mapping
View contacts on Maps tab
Maps tab can be undocked
Relocatable / resizable
Free mapping – OpenLayers
Can choose other with API Key from mapping vendor

## Slide 30: YCAT – Spectrum Scope
Limited to FT-710 and FT-dx10 radios
Allows controlling rig display from YCAT
Helpful if using DVI-D to USB Video Capture device

## Slide 31: YCAT – Example of PMS
Example of Extra class operator transmitting on band edge for Advanced class
When setting rig for Preferred Memory it keeps you within the limits you set.
I tried tuning to QSO but my lower limit is 14.175 MHz

## Slide 32: YCAT - FT8 Operation
Laptop display with WSJT-x, YCAT mapping / Logbook
Requires a virtual serial cable between WSJT-x and YCAT’s EXT Serial interface.

## Slide 33: YCAT – Questions / answer
Open for Q/A